# Spirometry using a mobile microphone
INTRODUCTION
This report will explore ways in which it might be possible to perform spirometry using a microphone, such as that of a mobile smartphone, and will describe early experiments investigating these possibilities.

Background information
Spirometry
Spirometry is the measurement of lung function. A subject is commonly asked to perform a “forced expiratory manoeuvre”, where a maximal inspiratory breath is taken and then air is forcefully expired at the greatest speed and to the greatest extent possible. The volume of the expired air is measured over time, allowing flow rate to be estimated as a function of volume. The shape of the graph of flow rate as a function of volume as shown in Figure X *** can be used by a respiratory clinician to help diagnose obstructive or restrictive pulmonary conditions. For example, in a patient with no respiratory disease, after the peak expiratory flow rate (PEFR), flow decreases almost linearly as a function of total expired volume until the full vital capacity (FVC) is reached.

***Figure X: example graphs of flow rate as a function of volume measured using spirometry. Left-hand panel: normal lungs; central panel: obstructive disease; right-hand panel: restrictive disease.

In a patient with an obstructive disease like asthma or chronic obstructive pulmonary disease (COPD), the decrease in flow after PEFR is concave as a function of volume, reflecting the pathological changes in resistance to flow through different parts of the lung. For these patients, the ratio of maximum forced expiratory volume after one second (FEV1) to FVC (FEV1/FVC) is usually smaller than for patients without respiratory disease, even though FVC may have a normal or near-normal value. Obstructive lung disease can be staged using the value of FEV1/FVC compared with expected values for the patient's age; for example, stage 1 is usually associated with a FEV1/FVC lower than 80% of that expected.

Restrictive diseases such as idiopathic pulmonary fibrosis (IPF) or respiratory muscle weakness show a convex decrease in flow rate as a function of volume, and PEFR and FVC are usually smaller than those patients without respiratory disease. For these patients, FEV1/FVC may have a normal or even high value.

Full spirometry is usually performed in a hospital or other specialist centre, with patients attending regularly so their lung function can be monitored over time. Outside hospital, PEFR is an important monitoring parameter for patients with lung disease because measurement can be carried out at home using a handheld peak-flow meter, which is a laminar flow tube with a sliding marker that is pushed along the tube by exhaled air. The PEFR can be read from the scale next to the sliding marker. As an example, patients with asthma are commonly asked to measure their PEFR every morning and evening to monitor their response to a change in medication regimen or steroid trial or to track diurnal variation, as a reduced PEFR in the morning compared to the evening is a common clinical feature of asthma. A 20% reduction in PEFR for a patient with cystic fibrosis (CF) is an indication for hospital admission (***ref); this can prevent the need for emergency admission, which is associated with a poorer prognosis as well as increased costs for a healthcare system.

Pneumotachometers
The most common device for performing spirometry in a hospital is a pneumotachometer. A patient performs a forced expiratory manoeuvre through the device, and pressure sensors before and after a known resistive element are used to calculate the change in pressure, which is proportional to the change in flow rate of the air.

Where laminar flow is seen, as in a Fleisch-type pneumotachometer, which uses a network of small-lumen capillaries to add resistance, the relationship between pressure drop and flow rate is almost linear. Where Venturi flow is seen, the relationship between pressure change and flow rate is quadratic. Calculated flow rate can be integrated with respect to time to find the volume of air expired during forced expiration.

***What happens in flow out of mouth, modelled as a circular hole in a sphere?

Pneumotachometric spirometers provide an accurate measure of lung function ***examples. However, at the present time, pneumotachometric spirometers are fragile and costly, and must be calibrated daily. For example, *** costs £***.

***Gupta et al MobileSpiro: pneumotach attached to smartphone

***Glynn et al $100 Fleisch-type spirometer

Microphone spirometry
A small number of authors have attempted to use a microphone to perform spirometry. Microphones transduce variations in air pressure to variations in voltage using a diaphragm. Where the forced expiratory manoeuvre is performed in a free field, that is, without the use of a mouthpiece to give laminar flow, the relationship between pressure (p) and flow rate (u) is nonlinear due to turbulence: flow rate through the lips is approximately proportional to the square root of the air pressure at the lips.

Larson et al. (***) developed SpiroSmart, a mobile phone application for iOS devices that uses the phone's microphone to capture a forced expiratory manoeuvre. They tested SpiroSmart using subjects with known normal and abnormal lung function, and compared the SpiroSmart's estimates of FVC, FEV1 and PEFR to those measured using a clinical pneumotachometric spirometer. While subjects could not use SpiroSmart and a pneumotachometer at the same time, three pneumotachometer measurements were recorded, and more SpiroSmart measurements were recorded (although the exact number was not reported). SpiroSmart measurements were compared with the pneumotachometer measurements, and were also compared with published limits of variability for each measure of lung function.

It was reported that, for normal subjects, SpiroSmart gave measurements of FVC that were within accepted clinical limits about 80% of the time and about 90% of the time for FEV1 and PEF. However, for subjects with abnormal lung function, measurements were within the accepted clinical limits about 65% of the time for all measurements. Larson et al. found that using machine-learning algorithms trained on data from repeat sessions for an individual subject improved the accuracy of estimates for subjects with abnormal lung function, falling within the accepted range 65% of the time for FVC and 80% of the time for FEV1 and PEFR. They called this machine-learning stage “personalisation”.

On closer inspection of the data in the study by Larson et al., it appears that the 95th centile of lung function measures showed a disparity between SpiroSmart and pneumotachometer measurements of between 10% and 13% for all measurements for normal subjects, and between 20% and 30% for abnormal subjects even after personalisation. This variation is outside the limit recommended by the American Thoracic Society (ATS) for clinical spirometry ***ref Standardisation of Spirometry. Eur Respir J. 2005;26:319–338. DOI: 10.1183/09031936.05.00034805) , but might be acceptable for home spirometry if the aim is to identify patients who need to be reviewed in hospital. Larson et al. noted that SpiroSmart calculations could not be performed on a smartphone in real time due to their complexity. ***we are less bad than this***

Aims of this report
The main aim of this report is to investigate the suitability of a smartphone's microphone to perform spirometry. The approach taken in the first instance was close to that of Larson et al., with some important modifications, which will be described in the method section. ***.

It is hoped that streamlining and extending the ideas of Larson et al. will allow the development of a spirometry algorithm that is accurate enough to be used for home screening as well as fast enough to be performed in real time on a smartphone.

A secondary aim is to establish the possibility of replacing regular use of a peak-flow meter with a smartphone application, as this might encourage patients to measure their PEFR more often. ***Say why this would be good***

METHOD
Setup
***sample rate
***deciding on beginning and end of manoeuvre: t0 and tmax by extrapolating back as in ATS spec
***etc

Feature detection
Envelope analysis
The microphone of a smartphone measures variations in pressure over time, p(t), which are uncalibrated in terms of absolute magnitude, but which are proportional to the different elements of the forced expiratory manoeuvre. The maximum value of p(t) during a forced expiratory manoeuvre will correspond to the PEFR, the integral of p(t) over the first second of the manoeuvre will correspond to FEV1, and the integral of p(t) over the whole manoeuvre will correspond to FVC.

We calculated the Hilbert envelope of p(t) and lowpass-filtered it to remove background noise using a 4th order Butterworth filter providing a gain of 1 up to a frequency of 26 Hz. The Hilbert envelope of the signal is the magnitude (modulus) of the complex analytic signal

y = x(t) + i.h(t)

where x(t) is the original signal, i is √-1 and h(t) is the Hilbert transform of the signal at time t; thus the Hilbert envelope E can be calculated as:

E(t) = √ [ x(t)2 + h(t)2 ]

[The Hilbert transform can be calculated by shaping ***its magnitude spectrum calculated by fast Fourier transform (FFT) and then calculating the inverse FFT of the result.  ***WHYYYYY]

The maximum value of the Hilbert envelope of p was taken to represent the PEFR.

Measurement of FEV1 and FVC were calculated from the integral of E with respect to time between t0 and t1 for FEV1 and between t0 and tmax*** for FVC.

Calibration
Since the exact nature of the proportional relationship between p(t) and the true value of the parameters PEFR, FEV1 and FVC is unclear, Larson et al. estimated the true value of the pressure at the lips, plips, by accounting for losses due to microphone distance and reflections from the subject's head and body using a transfer function derived from modelling the subject's head as a rigid spherical baffle in an infinite plane. The flow rate at the lips, ulips, was then calculated from plips using the relationship (omitting scaling constants):

ulips(t) ~ 2πr2√[2plips(t)]

where r is the radius of the mouth opening. While this method in theory protected against underestimating the size of differences in flow rate by attempting to deconvolve multiple quadratic relationships, it was computationally intensive: the algorithm could not run in real time on a smartphone, and was required to be run in the cloud. Furthermore, the method of Larson et al. was actually reported to overestimate some parameters for some subjects, which could be due to oversensitivity of the loss-reduction algorithm.

Here we made use of the fact that subjects can measure their peak flow accurately using a peak-flow meter. To calibrate our application, we measured the FVC of a nominated individual using a Micro Direct microloop spirometer, and used this to work out the scaling factors relating p(t) to the true expired volume.

***required a subject to perform three forced expiratory manoeuvres through their peak-flow meter and then to perform three using our application. We mapped the range of PEFRs measured using the peak-flow meter onto the range of measurements obtained from the microphone, and found that **

***Do we have to estimate the real sound pressures or can we get round it with maths and some known curves?
***If we have to estimate the real sound pressures, can we do less bad fluid dynamic modelling than a rigid sphere in an infinite plane? They say they compensated for reflections from the body, but the equation they give doesn't seem to do that
***How variable are our measurements? How variable is one measurement if our lowpass filtering (envelope smoothing) is done a different way? Does it matter which method we use to calculate the envelope, e.g. Hilbert, half-wave rectification etc